## Slide 1
Chapter 07 Flowchart of Single-camera Measurement
(Theme 2)
Prof. Lin ZHANG
School of Computer Science and Technology
Tongji University

## Slide 2: Problem definition of single-camera measurement
Can you tell me the diameter of the coin shown in the image?

## Slide 3: Problem definition of single-camera measurement
In this demo, the system detects persons and speed-bumps and outputs their horizon distances to the robot
Only one camera is used
How to achieve this goal?

## Slide 4
  To solve the aforementioned two problems, we need to have some assumptions
    The object to be measured should locate on a (physical) plane
    The imaging plane and the physical plane satisfy projective transformation, i.e., the imaging process should satisfy the ideal pin-hole camera model
There is a projective transformation matrix H linking the physical plane and the imaging plane. For a point x on the imaging plane, we can get its position on the physical plane as Hx
Problem definition of single-camera measurement

## Slide 5
Problem definition of single-camera measurement
x
y
u
v
Imaging plane
(unit: pixel)
physical plane
(unit: mm)
x
H

## Slide 6
Steps for achieving single-camera measurement
Calibrate the camera to get its intrinsic parameters
With the intrinsic parameters, un-distort the images to make the imaging process satisfy the ideal pin-hole imaging model
With a set of marker-points (their positions on the physical plane are known, and their images on the imaging plane are also known), get H
With H, for any point on the imaging plane, we can get its position on the physical plane

## Slide 7
Steps for achieving single-camera measurement
With H, to go one step further, we can generate the bird’s-eye view of the physical plane, which is very useful to perform detection and measurement of plane objects
The geometric transformation between the physical plane and its bird’s-eye view is a similarity transformation

## Slide 8
Steps for achieving single-camera measurement

## Slide 9: Contents of this theme
To study the camera calibration algorithm, we need to have some knowledge about projective geometry, which will be introduced in Chapter 8
Camera calibration is a non-linear least-squares problem; Chapter 9 will formally define such a kind of problem and the algorithms to solve it
Imaging model and the camera calibration algorithm will be detailed in Chapter 10
In Chapter 11, we will learn how to generate the bird’s-eye view for the physical plane

## Slide 10: Contents of this theme
数学
算法
应用
单目测距
平面目标测量
相机位姿估计
技术
视觉里程计
罗德里格斯公式
旋转的轴角表达
非线性最小二乘问题
阻尼法
射影几何
高斯牛顿法
列文伯格-马夸尔特法
相机成像流程建模
镜头畸变建模
相机内参平面标定法
相机内参标定
相机镜头畸变去除
鸟瞰视图构建
雅可比矩阵
凸函数
无穷远点与消失点
逆透视投影
鸟瞰环视图
场景三维重建
泰勒展开